## Slide 1: TOuNN : Topology Optimization using Neural Networks
Aaditya Chandrasekhar
Krishnan Suresh

## Slide 2
Paper: https://ersl.wisc.edu/publications/2020/TOuNN_Submitted.pdf
Code : https://ersl.wisc.edu/software/TOuNN.zip

## Slide 3: Topology Optimization
Consider classical SIMP TO,
SIMP TO
Cantilever Beam
Other approaches :
Level set
IGA
BESO…
How is material distributed over a given domain ?
{
{
Notes: Add movie of SIMP. Mention other approaches. Current focus is on SIMP based . Key concept: Mesh -> elem/node based capturing of field. Design variable is different/ capturing rho using NN!

## Slide 4: FE based SIMP– Design variable
Domain with B.C.
Discretize domain into mesh
SIMP : Element/node density
TO depends on mesh discretization
20 X 10 mesh
80 X 40 mesh
Notes: Level set : Phase field from mesh
BESO : Element on/off

## Slide 5: Key concept – TOuNN
Capture SIMP density using Neural Net
Independent of underlying mesh
Function of spatial coordinate
Global ( weights capture entire design )
How is material distributed over a given domain ?
{
{
NN Input
NN Output
Notes: Change the figure. New slide

## Slide 6: Implementation – Neural net
Fully connected
Batch norm observed to make the optimization more robust (even though full batch used)
Softmax function at output layer.
Notes: NN has built in optimizer and back prop facility. Comes down to min of loss. Constrained to unconstrained oprtimization bold w. Collection of all design variables.

## Slide 7
Optimization problem - overview
Notes: Densities indirectly defined from NN. All design var by w. Here we see constrained problem

## Slide 8: Implementation – Loss
Penalty param
Compliance
Vol constraint
Constrained Optimization Unconstrained Optimization

## Slide 9
Optimization problem - flowchart
1
2
3
4
5
Built in Gradient descent optimizer -Adam
Built in sensitivity calculation – Back propagation
{x,y} from mesh
iter
Loss
Notes: Talk about params -> # design variables.

## Slide 10: Result – Validation
Problem
SIMP
TOuNN
5 Layers ; 20 Neurons/layer ~ 1700 parms
60 X 30 mesh = 1800 elements/design var.
Notes: Talk about iteration. Performing better than SIMP. Show as movie, animation. PAUUSE ANIM AFTER OPTIMIZATION

## Slide 11: Validation – 3D, non-box geometry

## Slide 12: Neural net size ?
NN : 1 X 1 ( 6 parameters)
Captures simple geometry

## Slide 13: Features – Continuous density function
Obtain design at high resolution as postprocessing
(Low resolution mesh/sampling)
(High resolution mesh/sampling)
1
3
2
4
Notes: Simplify slide

## Slide 14: Obtaining boundaries
(SIMP)
Staircase boundary

## Slide 15
Obtaining boundaries - Backprop

## Slide 16: Extensions under consideration
Multi-material
Continuous fiber
Microstructure

## Slide 17: Multi-Material

## Slide 18: Continuous Fiber Optimization
X
Y
NN

## Slide 19: Summary
Used representational capacity of NN to perform TO.
No data as such. Simply used NN for function space.
Competitive to SIMP.
Clean, smooth and differentiable boundary.
Unique advantages to using NN function space.